## Slide 1
START
Prepare the Kjeldahl Distillation apparatus and glassware by cleaning and rinsing
Make ready all the required reagent standard solution of ammonia and American Chemical Society grade demineralised water
Select the required sample volume
Take 3 number Kjeldahl Distillation flask. 1st measure 50ml demineralised water for blank, 2nd measure 50ml standard solution and 3rd measured 50ml water sample
Take 3 conical flask of 500ml. Add 50ml boric acid and mixed indicator in all 3 flask
Make sure all the connections correct and leak proof
Start the distillation till boric acid and mixed indicator conical flask become 200ml distillate. Cool the distillate and titrate against 0.2 sulphuric acid standard solution . Unit solution turn pale lavender colour and note down the reading for calculation
Compare the standard solution value to experiment if error < 5% report the concentration of water sample
End